# Computation time optimization

The figure below shows how the precision of box model results can be computed at set precision and with optimized computation time.

Illustration 1: Optimization of comutation time

Fig. 1 shows how the individual processes in the box model are calculated post each other. Before a process is entered, the respective entry of vector n_speed is checked (represented by “N”). In case its value is larger than 1, the process is not called at each repetition of the loop (e.g.: if n_speed(2) = 4, nucleation is called on first loop repetition and the next time at 5th repetition. Further, nucleation is calculated for 4*dt_box). After calculating a process, characteristic parameters of the process are compared to the set precision limits of the process. This is illustrated by “P” which can be found below each process box in the figure. In case the desired precision is achieved the loop continues and the next process is calculated. If the precision is not high enough the current repetition of the loop is stopped and the integration time step is divided by two. In order not to increase precision of the calculation of the other processes (and thereby wasting computation time) the n_speed entry of all other processes is multiplied by two. That way the integration time step is solely increased for the process requiring higher precision. This process also allows to lower increase the integration time step for individual processes in case the precision achieved is much too high. As a result the simulation proceeds at high timely resolution when it is required and at low timely resolution in case the change rates are low.
The incrementation of the model time (i.e. the numerical integration) is only performed in case all precision parameters are within the required limits. When the sim_time is reached the loop terminates.